Semesterprojekt Mobile Anwendungen
von
Steven Bradley und Tobias Kolb

---
Thema...
6LoWPAN
IPv6 over Low power Wireless Personal Area Network

---
THE TASK
Find a way to program a CC2531 and set it up as a node in a 6LoWPAN multi-Hop Network

---
TI CC2531 USB dongle

---
6LoWPAN Multi-Hop Network

---
Network Stack
Layer	Protocoll
Application	-
Transport	udp-socket.c (simple-udp.c)
Network, Routing	uip6.c, rpl.c
Adaptation	sicslowpan.c
Mac Layer	csma.c
RDC Layer	nullrdc.c
radio	cc2530-rf.c

---
The Toolchain
Idea 1:
Q: Is there proprietary software that we can use?
A: Yes (IAR Embedded Workbench), but it's 3000 per license , per machine. So no.

---
The Toolchain
Idea 2:
Q: Is there Open Source Software we can use?
A: Yes (SDCC - Small device c compiler). However we needed a custom version, not the standard issue SDCC.

---
The Toolchain
Idea 3:
Q: If these approaches did not yield any results: are there others who might have tried and developed software for this purpose?
A: Yes (Contiki). It does use the SDCC, but embedded in a working, pre-made toolchain. When setup manually SDCC has to be compiled, which we did, later on.

---
Contiki Sensinode
- Operating system for networked, memory-constrained systems with a focus on low-power wireless IoT devices.
- Extant uses for Contiki include systems for street lighting, sound monitoring for smart cities, radiation monitoring, and alarms.
- Open-source software released under a BSD license.
- ARM accquided Sensinode, the developer of Contiki Sensinode in Aug 2013.

---
AT Commands
- AT commands are instructions used to control a modem
- AT – short for Attention
- answers with OK or FAIL
AT+PID 1024
AT:	prefix that informs the modem about the start of a command line
+PID 1024:	sets the current pan_id to 1024
+PID:	shows the current pan_id

---
IEEE 802.15.4 Radio settings
Command	Parameters	Range	Description	Result
AT+TXPWR	[TX_POWER]	5 to 28	Sets or shows the current TX_Power.	[TX_POWER] / OK
AT+SCH	[CHANNEL]	11 to 26	Sets or shows the current RF channel.	[CHANNEL] / OK
AT+PID	[PAN_ID]	0 to 65535	Sets or shows the current pan_id.	[PAN_ID] / OK
AT+RSSI	-	-	Returns the current received signal strength indicator (RSSI)	{RSSI} / OK/FAIL

---
The way ahead
1. Get multiple nodes to communicate to each other
2. Build app that uses a serial interface to exchange data with the dongle via an OTG-adapter

---
Repository
 https://github.com/BlkPingu/zigPAN